## Slide 1: Introduction to MODFLOW 6
Advanced MODFLOW Training Class, November 22, 2024, Deltares, NL

## Slide 2: MODFLOW 6 Objectives
Provide a single program that consolidates simulation capabilities in the numerous MODFLOW variants, including, for example:
  MODFLOW-2005
  MODFLOW-LGR
  MODFLOW-NWT
  MODFLOW-USG
  SEAWAT
  GSFLOW
Support multiple model instances and multiple model types in a single simulation
Provide a platform for extending MODFLOW into a configurable hydrologic simulator

## Slide 3: Range of Scales for MODFLOW Applications
bench
site
subregional
regional
national
global

## Slide 4: MODFLOW 6 Components
Models
Exchanges
Solutions
Timing
Simulation

## Slide 5: Model Types
Groundwater Flow (GWF)
Groundwater Transport (GWT)
Published
Groundwater Energy Transport (GWE)
Coming soon
Particle Tracking (PRT)
Surface Water Flow (SWF)
Watershed
Linear Network Flow (LNF)
In development

## Slide 6: Groundwater Flow (GWF) Model
Highlights
  Structured or unstructured grids
  Newton or standard formulation
  Full 3D anisotropy (XT3D)
  Compaction and subsidence (CSUB)
  Multiple stress packages of the same type
  Advanced stress packages (SFR, LAK, MAW, UZF)
  Water mover (MVR)

## Slide 7
Storage (STO)
Node Property Flow (NPF)
Horizontal Flow Barrier (HFB)
Specified Head (CHD)
Observations (OBS)
Recharge (RCH)
Output Control (OC)
Discretization (DIS, DISV, DISU)
Initial Conditions (IC)
Well (WEL)
Groundwater Flow (GWF) Model
Data Input
Internal Flow
Hydrologic Stress Package
Internal Flow
Stream-Flow Routing (SFR)
Multi-Aquifer Well (MAW)
Lake (LAK)
Advanced Stress Package
Unsaturated Zone Flow (UZF)
Water Mover
(MVR)
Compaction and Subsidence (CSUB)
Ghost Node Correction (GNC)
River (RIV)
General-Head Boundary (GHB)
Evapo-transpiration (EVT)
Drain (DRN)
Buoyancy (BUY)
Viscosity (VSC)
Notes: This is the structure of the GWF Model in MODFLOW 6
If you haven't used MODFLOW 6 before, it's very similar to previous MODFLOW versions; however,
We added a few things; we took a few things out.
We continuously ensure that MF6 gives the same answers as mf2005, mfnwt, mfusg (and if not, then why not)
MODFLOW 6 was developed as an object-oriented program:
To you, this means you can have more than one instance of certain things, like packages and models
Packages are objects, so we can have more than one package of the same type (when it makes sense). Not a big deal, but possibly useful
Simulation can have more than one GWF Model
LPF -> NPF, STO, ...

## Slide 8: Groundwater Transport (GWT) Model
Highlights
  Structured or unstructured grids
  Advection, dispersion, sorption, decay/growth
  Mobile and immobile domains
  Advanced packages (SFT, LKT, MWT, UZT)
  Water mover for transport (MVT)

## Slide 9
Mobile Storage and Transfer (MST)
Advection (ADV)
Dispersion (DSP)
Source and Sink Mixing (SSM)
Observations (OBS)
Constant Concentration (CNC)
Output Control (OC)
Discretization (DIS, DISV, DISU)
Initial Conditions (IC)
Immobile Storage and Transfer (IST)
Flow Model Interface (FMI)
Mass Source Loading (SRC)
Mobile Domain
Immobile Domain
Groundwater Transport (GWT) Model
Data Input
Internal Transport
Internal Transport
Solute Stress Package
Internal Transport
Streamflow Transport (SFT)
Multi-Aquifer Well Transport (MWT)
Lake Transport (LKT)
Advanced Solute Stress Package
Unsaturated Zone Transport (UZT)
Mover Transport
(MVT)

## Slide 10: Exchanges
Communication between any two models occurs through an ”exchange”
Exchange types include:
  GWF-GWF: connects two GWF Models
  GWT-GWT: connects two GWT Models
  GWF-GWT: provides the simulated flows from a GWF Model to a GWT Model
MODEL
MODEL
EXCHANGE

## Slide 11: Solutions
Dependent variables for one or more models are calculated by a “solution”
A focus of MODFLOW 6 has been on the Iterative Model Solution (IMS)
IMS solves for head (GWF) or concentration (GWT)
MODEL
MODEL
EXCHANGE
SOLUTION

## Slide 12: Exchange Data
Connect two GWF models by specifying a GWF-GWF Exchange in the configuration
Exchange file contains geometrical data for connection between neighboring nodes
Ln
n
m
Lm
Δw
Model 1
Model 2
Notes: A user can couple two GWF models by specifying a GWF-GWF exchange. The exchange file contains geometrical data for how cells are connected across models.

## Slide 13: Generalized Control-Volume Finite-Difference Numerical Solutions

## Slide 14: Single-Model Configurations
Simulation
Numerical Solution
Groundwater Flow Model
Temporal Discretization
Simulation
Numerical Solution
Groundwater Transport Model
Temporal Discretization

## Slide 15: Multi-Model Configurations
Simulation
Numerical Solution
Groundwater Flow Model 1
Temporal Discretization
Groundwater Flow Model 2
GWF-GWF Numerical Exchange
Simulation
Numerical Solution 1
Groundwater Flow Model
Temporal Discretization
Groundwater Transport Model
GWF-GWT Exchange
Numerical Solution 2

## Slide 16: Multi-Model Configurations
Simulation
Numerical Solution 1
Groundwater Flow Model 1
Temporal Discretization
Groundwater Flow Model 2
GWF-GWF Numerical Exchange
Numerical Solution 2
Groundwater Transport Model 1
Groundwater Transport Model 2
GWT-GWT Numerical Exchange
GWF-GWT
Exchange 1
GWF-GWT
Exchange 2

## Slide 18: Summary
MODFLOW 6 is based on the concept of models, exchanges, and solutions
For users, the underlying model/exchange/solution architecture provides flexibility for configuring complex multi-model simulations
The new parallel capabilities build on these concepts to allow simulation of multiple models in parallel

## Slide 19: MODFLOW 6 Timeline
2013 – Initiated development
2017 – First release with the Groundwater Flow (GWF) Model
2020 – MODFLOW Application Programming Interface (API)
2020 – Release of Groundwater Transport (GWT) Model
2023 – Release of parallel simulation capabilities
2024 – …